## Slide 1
Smart Home IoT System
A full-stack IoT system integrating real hardware sensors with unified automation and control
Project Team: Muhammad Omais Rana, Muhammad Shiraz
December 17, 2025

## Slide 2
Table of Contents
The Vision: Unified Home Automation
System Architecture
Multi-Protocol Network Stack
Sensor Data Collection
Node-RED Hardware Automations
Laravel Business Logic
Hybrid Data Strategy
Dual Dashboard System
Future Enhancements

## Slide 3
The Vision: Unified Home Automation
Monitor
Track environmental conditions with Temperature & Humidity sensors
Surveil
Live MJPEG video feed for premises security
Simulate
Virtual Door Sensor using Digital Twin concept
Automate
Respond to environmental hazards with smart alerts
Notify
Email alerts for security breaches and events
Unlike proprietary systems, this open-source architecture provides a single interface to control your entire home ecosystem.
2

## Slide 4
System Architecture
Hardware Layer
ESP32 Sensor Node controls four actuators:
Main Light
AC Indicator
Mold Alert
DHT11
ArduCAM Vision Node streams live MJPEG video
Processing Layer
Node-RED: Hardware automation brain running parallel flows
InfluxDB: Time-series sensor storage
MySQL: Relational device state management
Application Layer
Laravel: Primary control center and user interface
Grafana: Historical analytics and trend visualization
3

## Slide 5
Multi-Protocol Network Stack
MQTT
Lightweight Publish/Subscribe model for real-time sensor data and control commands. ESP32 publishes telemetry and subscribes to command topics.
HTTP
Handles media streaming (MJPEG video), database queries, and web dashboard delivery across the network.
SMTP
Laravel connects to mail servers to dispatch security alert emails when door status changes are detected.
TCP/IP Wi-Fi
Provides the underlying transport layer connectivity for all devices on the smart home network.
4

## Slide 6
Sensor Data Collection
1
Temperature & Humidity
Source: Real data from DHT11 sensor
Sampling Rate: Every 5 seconds
Purpose: Environmental monitoring and AC automation
2
Visual Feed
Source: Real data from ArduCAM
Format: MJPEG Stream over Wi-Fi
Purpose: Live premises surveillance
3
Door Status
Source: Synthetic data via Dashboard Toggle
States: 0=Closed, 1=Open
Purpose: Security event simulation and notification testing
5

## Slide 7
Hybrid Data Strategy
Real Physical Data
Temperature readings from DHT11 sensor
Humidity measurements from DHT11 sensor
Video feeds from ArduCAM hardware
Provides authentic environmental monitoring and surveillance capabilities
Synthetic Simulation
Door Sensor simulated via software toggle
Tests Laravel SMTP notification pipeline
No physical magnetic reed switch required
Enables testing of security workflows without additional hardware
6

## Slide 8
Node-RED Hardware Automations
Node-RED handles "fast" logic close to the hardware with three distinct automation flows:
1. Data Pipeline
Ingests raw JSON from MQTT and writes to InfluxDB for historical analysis.
2. Smart AC Control
Activates AC (Blue LED indicator) if temperature exceeds 27°C.
3. Mold & Hazard Alert
Activates Red LED warning if humidity exceeds 40%.
6
7

## Slide 9
Laravel Business Logic
Security Notification System
Trigger: Listens for state changes in MySQL table (Virtual Door)
Action: When state changes to 1 (Open), Laravel queues a job to send email via SMTP to homeowner
Purpose: Event-driven alerting for security breaches
8

## Slide 10
Dual Dashboard System
Operational Dashboard
Platform: Laravel
Functions: Controls Main Light, monitors Door status, displays live Video feed
Purpose: Real-time device control and monitoring
Analytical Dashboard
Platform: Grafana
Functions: Visualizes historical Temperature and Humidity trends from InfluxDB
Purpose: Long-term pattern analysis and insights
9

## Slide 11
Future Enhancements
Predictive HVAC Control
Use Machine Learning on InfluxDB data to activate AC based on historical daily patterns rather than simple temperature thresholds
Computer Vision
Process camera feed to distinguish between authorized residents and intruders using facial recognition
Energy Optimization
Correlate "AC On" duration with temperature drops to calculate room insulation efficiency and reduce energy consumption
10